## Slide 1
Insert your text Here
Insert your text Here
Insert your text Here
Insert your text Here
Insert your text Here
OFDM Transceiver using GNU Radio and SDR
.
Supervisor : Dr. Ramesha
.
Abstract
Background
Methods
Results
Conclusion
Future Perspectives
Future work should focus on enhancing OFDM transceivers with better synchronization, error correction,. Expanding to MIMO-OFDM for 5G and optimizing performance through real-world testing are key. Research should prioritize energy-efficient SDRs and secure, multi-standard systems compatible with Wi-Fi and 5G.
The development and implementation of an OFDM transceiver using SDR technology have demonstrated its viability in modern wireless communication. Utilizing GNU Radio and the USRP B210 platform, the transceiver successfully addressed challenges in synchronization, channel estimation, and error correction. Real-world testing provided insights into optimizing SDR systems for diverse environments..
Software Tools: GNU Radio Companion (GRC) for flowgraph development.
Hardware: USRP B210 for data transmission and reception.
Implementation: The OFDM transceiver was designed and simulated using GRC, focusing on key aspects such as symbol timing synchronization, frequency offset correction, and channel estimation.
Testing: The system was tested under various channel conditions to evaluate its performance in real-world scenarios.
Optimization: Adaptive modulation and coding techniques were explored to enhance system robustness and efficiency under changing channel conditions.
Insert
This project explores the design and implementation of an Orthogonal Frequency Division Multiplexing (OFDM) transceiver using Software-Defined Radio (SDR) technology, leveraging the GNU Radio framework. The project aims to demonstrate a functional SDR-based OFDM transceiver capable of transmitting and receiving data over the air. The implementation is carried out using GNU Radio, an open-source toolkit, which provides a flexible and cost-effective platform for developing communication systems.
  The rise of SDR has revolutionized how communication systems are designed, offering a flexible and reconfigurable approach to implement various modulation schemes. OFDM, a key technology in modern wireless systems, is known for its efficiency and robustness against multipath interference.
  This project aims to leverage GNU Radio and USRP B210 to implement and test an OFDM transceiver, exploring the practical aspects of SDR.
team members name :- Hari Priya Rao M ,Hamsini Reddy K S ,Kiran P S ;